## Slide 1: Sampling-Based Gaussian Estimation of Probability of Collision for Safe Planning
Ajaay Chandrasekaran
April 16, 2018
Notes: Published in 2012 IEEE International Conference on Robotics and Automation

## Slide 2: Research Motivation
Wish to quantify the safety of a motion plan before execution
  Applications range from autonomous vehicles to the PR2 robot
Many planners compensate for the possibility of a collision
Notes: Can be used inside a planner as a metric.
Emphasize safety in the context of obstacles
Safety is difficult to guarantee due to real world noise
The Astar path algorithm returns a shortest path, but not necessarily a safest path!
Why is this hard?

## Slide 3: Problems
Real world uncertainty in
  Robot motion
  Sensor information
Monte-Carlo simulation takes too long
  Requires many simulations of many particles
Collisions are dependent events
Motion Noise
MC Simulation
Notes: Monte carlo simulation: millions is too high
Execute a controller that simulates individual particles. Too expensive. One simulation = generate a million particles, then you have to simulate the million particles with noise. See what proportion of particles had a collision = p of collision for that simulation. Then, average all of the p’s of collision
Conservative: Underestimate of the probability
Can’t tree collision probabilities as independent events, otherwise you’ll highly overestimate the probability of collision with general analytical approaches that try to multiply proportions of particles colliding in individual particle distributions. Monte-Carlo would be more accurate in this case

## Slide 4: Goal
Quantify safety of a motion plan by accurately and quickly estimating the probability of a collision in presence of uncertainty
Time index
Number of waypoints
State at time index, t
State space
Free space
Notes: Conservative: If we are too conservative, planner will fail. If not conservative, then we expect more safety than there is.
Quickly: Must be efficient so that planner can run real time.

## Slide 5: Outline
Prior Work
Proposed Method
  Formulation
  Approach
    Gaussian Mixture Model Estimate Representation
    Rejection Sampling for Distribution Truncation
Results (So Far)
  PR2-Robot

## Slide 6: Prior Work
Constraint-based Gaussian Truncation
  Linear chance constraints (Du Toit et al., RO ‘11)
  Truncate a priori probability distributions along motion plan (Patil et al., ICRA ’12)
  Caveats:
    Assumes that we can form linear obstacle constraints in work-space
    Generalizes only to point-robots
    Patil’s method can degenerate in non-convex environments
Distance to Obstacle Check (van den Berg et al., RSS ‘10)
  Caveat:
    Incorrectly assumed independence between collision events along motion plan
Patil, ICRA ‘12
van den Berg et al., RSS ‘10
Notes: Problem: Assumes independence!
Emphasize that this approach accounts for independence
Vanden berg’s approach uses distance to obstacle checker to compute probability of collision
Du Toit’s approach looks at probability of violating constraints. Do you know constraints?
My work attempts to solve both problems. Consider dependence of collisions and also handle fact that we have a C-Space

## Slide 7: Outline
Prior Work
Proposed Method
  Formulation
  Approach
    Gaussian Mixture Model Estimate Representation
    Rejection Sampling for Distribution Truncation
Results (So Far)
  PR2-Robot

## Slide 8: Formulation: Gaussian Uncertainty
Robot operating in uncertain environment with obstacles
Motion Model
Sensor Model
: Robot State
Control input
Sensor measurement
Gaussian random noise variable with variance
Gaussian random noise variable with variance

## Slide 9: Formulation: Nominal Motion Plan
Given a nominal plan , where

## Slide 10: Formulation: EKF State Estimation
  Nominal robot state
  : True robot state
Estimate of true robot state

## Slide 11: Formulation: Linear Feedback Control
  Nominal robot state
  : True robot state
Compute , deviation from nominal control
)
  : Control gain

## Slide 12: Outline
Prior Work
Proposed Method
  Formulation
  Approach
    Gaussian Mixture Model Estimate Representation
    Rejection Sampling for Distribution Truncation
Results (So Far)
  PR2-Robot

## Slide 13: Overview of Approach
Cycle of propagation and truncation
  Propagation of a Gaussian mixture estimate of robot state distribution
  Sampling-Based Truncation of estimated robot state distribution
Attempt to capture distribution more accurately with multiple Gaussians
Notes: GOAL: We want to truncate distribution to better capture non-Gaussian distributions!

## Slide 14: Approach: Gaussian Mixture Model Estimate
Maintain mixture of Gaussians
  Weights: ,
  Mixture:

## Slide 15: Approach: Gaussian Mixture Model Estimate
Step 1: Initialize Gaussians with equal weight and same initial mean (start state) and covariance

## Slide 16: Approach: Gaussian Mixture Model Estimate
Step 2: Propagate individual Gaussians via motion model to next waypoint and update estimates via EKF

## Slide 17: Approach: Rejection Sampling Truncation
Step 3: Sample particles from mixture model using weights .
Notes: This is the C-Space. We don’t have to explicitly form the C-Space

## Slide 18: Approach: Rejection Sampling Truncation
Step 3 (cont.): Total proportion of colliding particles estimates conditional probability of collision for current waypoint
Notes: This is the C-Space. We don’t have to explicitly form the C-Space

## Slide 19: Approach: Rejection Sampling Truncation
Step 4: Update mixture weights to be proportions of total non- colliding particles for the waypoint
Notes: This is the C-Space. We don’t have to explicitly form the C-Space

## Slide 20: Approach: Rejection Sampling Truncation
Step 4: Compute analytical mean and covariance of non-colliding configurations in each Gaussian and approximate as new Gaussian
Notes: This is the C-Space. We don’t have to explicitly form the C-Space

## Slide 21: Approach: Rejection Sampling Truncation
Step 5: Repeat Step 1 and propagate estimated truncated distributions
Notes: This is the C-Space. We don’t have to explicitly form the C-Space

## Slide 22: Approach: Notes
Multiply proportions of colliding particles for all waypoints to estimate total probability of collision
Approach Justification
  Multiple Gaussians may capture truncated distributions better
  Sampling in C-Space with collision-checking permits non-point robots
  No requirement for already-known obstacle constraints

## Slide 23: Outline
Prior Work
Proposed Method
  Formulation
  Approach
    Gaussian Mixture Model Estimate Representation
    Rejection Sampling for Distribution Truncation
Results (So Far)
  PR2-Robot

## Slide 24: Evaluation: PR2 Robot
State and Control
u =
Odometry Motion Model
Sensor Model
Robot x position
Robot y position
: Robot orientation
Distance to landmark
: Landmark x position
: Landmark y position
: Rotation 1
: Translation
: Rotation 2
: Gaussian Noise Variables
Thrun et al., Probabilistic Robotics, Chapters 5,6
Notes: Odometry Motion Model as described by Thrun

## Slide 25: Experiment Setup
Implementation Details
  Nominal plan computed using A* Algorithm in OpenRave
  C++ implementation on 4-core Intel 2.20GHz i5 PC
Green Dots: Beacons for localization
Black Dots: Nominal motion plan

## Slide 26: Experimental Results So Far
Monte Carlo Simulations of 10,000 particles to gauge ground truth probability of collision
  N: 100 simulations
  Min: 0.8423
  Max: 0.9995
  Mean: 0.9399
  Std. Dev: 0.0416

## Slide 27: Experimental Results So Far (Cont.)
Time (sec) required for Monte Carlo Simulations of 10,000 particles
  N: 100 simulations
  Min: 103.6552
  Max: 121.5551
  Mean: 112.6999
  Std. Dev: 4.0729
Total time: ~3 Hours
Notes: Our goal is to beat the amount of time of doing the monte carlo simulations.
Ideally, may take same amount of time as one simulation and provide a good estimate of probability of collision

## Slide 28: Conclusion and Future Work
Presented a method to compute probability of collision, which
  considers conditional dependence of collisions
  does not require linear constraints to represents obstacles
  handles non-point robots given collision-checker
Next Steps
  Implement method and compare to Monte Carlo Simulation ground truth
  Test other environments
  Test accuracy among different motion plans
Notes: Method is applicable to wide variety of m planning under uncertainty methods

## Slide 29: End